; USBradio configuration

;		 -- YOU MUST CHOOSE: USBRADIO OR SIMPLEUSB OR VOTER –

;		USBRADIO uses CPU processing for COS and CTCSS decode (THIS FILE)

;		If you have COS available from radio, SIMPLEUSB is a better choice

;		If you are using an RTCM, then you must choose VOTER

;

; K5TRA BBB    27 August 2014

[general]

[usbXXXXX]				; usb stanza:   XXXXX is YOUR node number

hdwtype=0				; USB sound fob such as DMK URI

rxboost=0				; 20 dB pad inserted in audio stream from receiver (=1, no pad)

txboost=0				; 20 dB pad inserted in audio stream to transmitter (=1, no pad)

rxctcssrelax=1				; reduce talkoff from radios without PL filter

txctcssdefault=100.0			; default TX CTCSS freq, any frequency permitted

rxctcssfreqs=100.0,123.0		; RX CTCSS freq, any frequency permitted

txctcssfreqs=100.0,123.0		; TX CTCSS freq, any frequency permitted

;rxctcssoverride=0			; (=1, carrier squelch)

carrierfrom=dsp			; COS sense from DSP in CPU

ctcssfrom=dsp				; CTCSS decode from DSP in CPU

rxdemod=flat				; de-emphasize discriminator audio  (also  =speaker, or  =no)

txprelim=yes				; pre-emphasis of TX audio (alternatively, =no)

txlimonly=no				; (=yes, TX audio limited but not pre-emphasized)

txtoctype=phase			; TX tone control: reverse burst (alternatively, =no, or =notone)

txmixa=composite			; transmit audio on ‘a’ output from URI

txmixb=0				; URI ‘b’ output not used

invertptt=0				; PTT pull down to key  (=1, pull-up to key)

duplex=1				; full duplex

rxondelay=0				; no delay after transmit

rxnoisefiltype=0				; full RX audio bandwidth

eeprom=0				; no EPROM present in URI

#includeifexists custom/usbradio.conf